## Slide 1
Cruise Control: An HLS Auto-Optimzation Tool
Thomas Furlong, Andrew Smith
ECE 527 Final Project

## Slide 2
HLS is a great tool for rapid prototyping, development and optimization of custom hardware accelerators
Optimizing the performance is still a very manual process of placing pragmas at specific points in the code with trial and error
Challenge

## Slide 3
Design a tool to explore design space and produce a “good” result
Reduce the effort required by designers to create an efficient accelerator
Goal

## Slide 4
A design tool that can parse HLS source code and automatically evaluate different pragma placement permutations for an efficient solution
Cruise Control

## Slide 5
Approach

## Slide 6
Approach: Input Parser

## Slide 7
The TCLer
  Uses Vivado HLS TCL interface
  Minimal set up time
  Synthesizes every pragma placement
  Writes design statistics to report file
Approach: TCLer

## Slide 8
Enables the designer to choose highest performing design
Outputs a CSV file for easy analysis in Excel
Can then choose output that’s best suited for application’s physical constraints
Approach: Output Parser

## Slide 9
The current tool can find an optimal solution, but exhaustive search scales poorly
With the number of loops in a small accelerator easily exceeding 9, which leads to ~512 search states
We want to implement simulated annealing or a smarter search that throws out states based on the data we’ve collected so far
Current State

## Slide 10
Cannot analyze power without first placing and routing a netlist
  Not clear how to do this through TCL
Debugging TCL scripts is time consuming
Windows…
Challenges

## Slide 11
Design Space Analysis

## Slide 12
Results: Speed Up
mat_mul: 7.35x
lenet_conv5: 1.85x
lenet_fc6: 1.73x

## Slide 13
Drastically reduces designer effort
Cruise control can evaluate 15 permutations of pragma placements in the same amount of time a designer can evaluate 1
7.9 seconds per iteration
15x improvement in human efficiency
Can multitask while CruiseControl runs in background
Results: Designer Effort

## Slide 14
Smarter search strategy
  Simulated annealing
  Throw out states known to be bad
Power Optimization
  Need valid place & route
Different loop unrolling factors
  Optimize based on size of loop
Improve user experience
  Integration into Vivado HLS GUI
Future Work

## Slide 15
Q/A